## Slide 1: Controllers

## Slide 2: Analogue vs Digital Signals Reminder
For this lesson we are focusing on electrical signals which are split into two forms:
  Analogue signals are continuous and change smoothly over time
  Digital signals are discrete and therefore have set values which they change between

## Slide 3: PWM Reminder
  A technique to control power by rapidly switching a signal between ON and OFF states.
  Simulates an analogue output using a digital signal
  Used for controlling motors, LEDs, and power regulation

## Slide 4: What are controllers?
  Controllers are objects that link to sensors and actuators
  They facilitate communication between sensors and actuators
  They allow us to perform calculations with sensor inputs

## Slide 5: What are microcontrollers?
  Microcontrollers are small computers that act as controllers
  They differ from most regular computers as they are optimised for a specific task
  They often have lots of I/O (input/output) ports for communicating with lots of sensors and actuators

## Slide 6: Components of a microcontroller
  Micro controllers are made of the following key components:
      Central Processing Unit (CPU):
            The brain of the microcontroller
            Processes instructions and controls everything
      Memory:
            ROM (Read-Only Memory): Stores the program/code permanently.
            RAM (Random Access Memory): Temporary memory for running tasks.
      I/O Pins:
            Connects to the actuators and sensors

## Slide 7: Most Common Microcontrollers
  ATmega328P (Arduino Uno) – the most used microcontroller by both hobbyists and industry
  ESP32 – much more powerful than the ATmega328P includes built in Wi-Fi and Bluetooth capabilities
  STM32 – Used a lot for industrial and high-performance applications

## Slide 8: Picking a microcontroller
Microcontroller (price) | Clock Speed | Memory | Bit Size | GPIO Pins | Wifi/Bluetooth built-in | Power Usage | Use cases | Usability
ATmega328P (£22-£25) | 16MHz | 32KB Flash 2KB RAM | 8-bit | 23 | No | Low Power (15 mA) | Low power or battery powered | Easiest
ESP32 (£7-£9) | Up to 240MHz | 4MB Flash 520KB RAM | 32-bit | 34+ | Yes | Higher Power (160 mA) | Anything that needs wireless | Moderate
STM32 (£30-£35) | Up to 72MHz | 64-512KB Flash 20KB RAM | 32-bit | 37+ | No | Middle Power (30-100mA) | Industrial control | Difficult

## Slide 9: MicroComputers
  Microcomputers are miniaturised computers that are used for specific tasks
  They have a full OS allowing us to do much more complex tasks
  Most common are Raspberry Pi Series, BeagleBone Series and Jetson Nano
  They have higher power requirements than microcontrollers

## Slide 10: Picking a MicroComputer
Microcontroller | Price | Power Consumption | Processing Power | GPIO Pins | Best for
Raspberry pi 4/5 | £50-£100 | Most Power Hungry | Medium Power | 40 Pins | General purpose, all rounder
BeagleBone Black | £50-70 | Least Power Hungry | Least Powerful | 69 Pins | Industrial Control, Automation, Robotics
Jetson Nano | £80-£120 | Medium Power Hungry | Most Powerful | 40 Pins | AI, Machine Learning, Computer Vision

## Slide 11: Microcontroller vs Microcomputers
  We need a microcomputer when we are doing anything which needs significant processing power
  For instance, if we wanted to detect an animal on a video feed, we would need a microcomputer as microcontrollers are not powerful enough